## Slide 1
Intro
Project: security-aware digital twin for UGV01 rover sensor trust.
Hardware path is active: UGV01 tracked rover with BN220 GPS on verified RX wiring.
Week 1 instrumentation is complete: combined telemetry, timestamps, packet health, and replay path.
Week 2 motion/calibration work is complete enough to move into benign baseline collection.
Current milestone: collect Week 3 benign runs before locking thresholds or running attacks.
Digital Twin Divergence advisor update - July 16, 2026

## Slide 2
Motion Tests That Will Be Done
Primary Week 3 route: 0.5 m square loop repeated 3 times per trial.
Each loop closes with a fourth 90 degree turn so the rover ends facing its starting direction.
Validation sequence also covers forward 1 m, reverse 1 m, 360 turn, forward run, 180 turn, return run, and heading restore.
Slow timed quarter-turns are used because fast host-side HTTP turns overshot during testing.
Runs are valid only if the route completes without manual rescue and telemetry remains replayable.
Digital Twin Divergence advisor update - July 16, 2026

## Slide 3
Benign Dataset Environments
Smooth surface: kitchen floor.
Rough surface: permeable concrete.
Speeds: low and medium command settings, mapped to measured behavior during analysis.
Network conditions: baseline Wi-Fi and edge-side buffered-delay condition.
Target benign matrix: 2 speeds x 2 surfaces x 2 network conditions x 5 trials = 40 valid runs.
Digital Twin Divergence advisor update - July 16, 2026

## Slide 4
How The System Works
Firmware command T:147 returns combined base, encoder, IMU, voltage, GPS, sequence, sample, and send timestamps.
Bench logger adds edge send/arrival/estimate/alarm timing, clock-offset calibration, packet loss, stale-packet flag, and queue depth.
Digital twin replays real logs through tracked-drive kinematics, EKF state estimation, and Mahalanobis innovation detection.
Detector outputs include threshold comparison, lambda_max(S), epsilon_min, confidence, and envelope region.
Latency/jitter is emulated edge-side so rover behavior and firmware remain unchanged during network-condition tests.
Digital Twin Divergence advisor update - July 16, 2026

## Slide 5
What's Left To Do Next
Collect the 40-run benign Week 3 dataset using the locked square-loop route and surface labels.
Replay all benign runs through the digital twin and generate packet-health, latency, and detector-consistency reports.
Lock the Mahalanobis threshold from benign data to meet P_FA <= 0.05.
Compare learned uncertainty against fixed/adaptive covariance using only benign data.
After thresholds are locked, run attack trials: step bias, replay, and freeze, then produce final plots and paper results.
Digital Twin Divergence advisor update - July 16, 2026