## Slide 1
Digital Twin Divergence
A security-aware Digital Twin for rover sensor trust
Advisor update | July 10, 2026
Crux: T:147 combined telemetry packet
Real rover-to-edge pipeline working
Future work = calibrated field validation
UGV01 + BN220 bench stack operational
Central claim: the project now has one usable telemetry interface that carries timing, motion, IMU, and GPS state into the digital twin and will support the full experiment campaign.

## Slide 2
Crux: Combined Telemetry Packet
The main measurement interface is the firmware response to T:147.
Identity + timing
Base / encoders
IMU attitude + raw motion
GPS state + health
Edge-side timing use
T:147 contents
T:147 returns seq, sample_ms, millis, send_ms, L/R, enc_left/right, battery voltage, roll/pitch/yaw, raw IMU channels, GPS fix/lat/lon/sat/hdop, and GPS checksum/character counters.
Digital Twin Divergence

## Slide 3
Why T:147 Matters
This packet is the single input record that drives the research pipeline.
Dead reckoning
enc_left and enc_right support tracked-drive calibration and motion estimation.
Uncertainty context
IMU variability, GPS quality, and timing stress feed the adaptive uncertainty logic.
Timing analysis
seq, sample_ms, send_ms, and edge timestamps support packet loss, stale-packet, queue, and latency analysis.
Detection pipeline
The same packet replays through the EKF and Mahalanobis detector without changing rover behavior.
Bench evidence
The clean July 9 run achieved 379/379 successful cycles, 0 drops, seq 0 -> 378, and GPS valid throughout.
Detector evidence
Replay detections stayed at 0; max Mahalanobis remained below threshold while satellites improved 8 -> 11 and HDOP improved 1.48 -> 0.92.
Interpretation
The packet schema is now good enough to support calibration, benign baselines, and later attack experiments.
Digital Twin Divergence

## Slide 4
What Has Been Completed So Far
The packet interface is now backed by working tooling and documentation.
Embedded path
ugv01_gps_dev is active; BN220 stayed on the original verified RX wiring.
Bench tooling
bench_logger.py records T:147 and adds source/sample, send, arrival, estimate, alarm, packet loss, stale, queue depth, and clock-offset fields.
Replay + reports
Hardware logs replay through the EKF/detector path and now have stationary GPS, latency, and replay-consistency reports.
Project prep
Firmware docs, log dictionaries, preregistered protocol, and tracked-rover calibration utilities are already in the repo.
Digital Twin Divergence

## Slide 5
What The Future Project Entails
The remaining work is a structured validation campaign built on T:147.
Phase 1
Battery-powered safety check and confirmation that T:147 behaves correctly under self-powered rover operation.
Phase 2
Tracked-drive calibration: left_meters_per_tick, right_meters_per_tick, effective_track_width_m, and heading_sign.
Phase 3
Benign baseline collection across speed, surface, and latency conditions to define normal detector behavior.
Phase 4+
Threshold locking, learned uncertainty comparison, attack trials, and final figures validating the detectability boundary.
Digital Twin Divergence

## Slide 6
Immediate Next Steps
The next milestone is moving from bench telemetry to calibrated motion data.
Install batteries and run the first lifted-track safety test.
Verify T:147 under self-powered operation: seq, GPS, IMU, encoder, and stop behavior.
Collect straight-line and in-place turn calibration runs from the same telemetry packet.
Begin benign field runs after calibration is locked.
Takeaway: the packet schema is in place, the bench path is working, and the rest of the project is now an experimental validation problem.
Digital Twin Divergence