## Slide 1
Digital Twin Divergence
Detectability limits for GPS spoofing on an edge-hosted UGV digital twin
Phase 0 software scaffold complete
EKF + attacks + uncertainty + analysis
Ready for UGV01 integration

## Slide 2
Problem and Motivation
Why this project exists
GPS spoofing can send syntactically valid but physically false coordinates.
Traditional packet/network checks may miss semantic sensor attacks.
A digital twin predicts rover motion and compares prediction against reported GPS.
The research question is not only whether attacks are detected, but when they become statistically hard to detect.
Core tension
More speed, rough terrain, and latency increase uncertainty.
More uncertainty makes attacks harder to distinguish from normal noise.
Research aim
Map the minimum detectable GPS manipulation size.
Identify safe, warning, and blind operating regions.
2

## Slide 3
What the Project Represents
A security-aware mobile digital twin
Digital twin
Software model of the UGV state.
Predicts where the rover should be.
Divergence
Difference between predicted state and physical GPS.
Measured through innovation and Mahalanobis distance.
Detectability limit
How large an attack must be to reliably stand out.
Driven by innovation covariance S_k.
Digital Twin prediction vs. reported GPS -> innovation -> detector -> confidence envelope
The contribution is a measurable security boundary, not just a working localization filter.
3

## Slide 4
End-to-End Architecture
Telemetry to detection
UGV01 sensors
Arduino packet
Serial / WiFi
Python parser
EKF twin
Detector + logs
Implemented sources
telemetry.py, kinematics.py, ekf.py
uncertainty.py, detector.py, attack.py
logger.py, experiment.py, plot.py
analysis scripts for P_D, ROC, threshold locking
Hardware adapter later
Firmware already serializes the packet shape.
Real GPS/encoder/IMU values replace synthetic placeholders.
4

## Slide 5
Telemetry Protocol
Frozen interface before hardware
Packed 76-byte little-endian TelemetryPacket with CRC32.
Fields include sequence, timestamp, encoder ticks, IMU, GPS, fix metadata, and HDOP.
Arduino serializer and Python deserializer use the same packet contract.
Synthetic simulator emits the same packet shape as future hardware.
Arduino Packet -> Serial/WiFi -> Python -> EKF/logs
Why this matters
Hardware arrival should be integration, not interface redesign.
CRC + sequence numbers expose packet corruption and drops.
5

## Slide 6
Rover Physics and Kinematics
Differential-drive motion
state x_k = [p_x, p_y, theta]^T
v = (Delta s_R + Delta s_L) / (2 Delta t) omega = (Delta s_R - Delta s_L) / (b Delta t)
p_x_next = p_x + v cos(theta_mid) Delta t p_y_next = p_y + v sin(theta_mid) Delta t theta_next = theta + omega Delta t
Interpretation
Equal wheel motion -> straight line.
Unequal wheel motion -> turn.
Wheel radius, wheel base, and ticks/rev must be calibrated on real UGV01.
What is implemented
DifferentialDriveGeometry converts ticks to controls.
Synthetic square, circle, and figure-eight trajectories are available.
6

## Slide 7
Extended Kalman Filter
Prediction plus GPS correction
Prediction
Use encoder-derived v and omega.
Propagate state and covariance.
P_pred = F P F^T + Q.
Update
GPS gives z = [gps_x, gps_y].
innovation nu = z - H x_pred.
K = P H^T S^-1.
Output
Corrected rover state estimate.
Innovation, S_k, Kalman gain, Mahalanobis distance.
CSV rows for analysis and plots.
S_k = H P_k|k-1 H^T + R_k
x_k|k = x_k|k-1 + K_k nu_k
7

## Slide 8
Detector Math
From innovation to attack evidence
delta_k = nu_k^T S_k^-1 nu_k
delta_k is Mahalanobis distance: error measured relative to uncertainty.
If delta_k exceeds the locked threshold, the detector flags an anomaly.
Under nominal operation, delta_k approximately follows a chi-square distribution.
epsilon_min = sqrt(lambda_star * lambda_max(S_k))
epsilon_min is the minimum reliably detectable GPS manipulation size.
As S_k grows, the detectable attack size grows.
This is the proposal's central detectability boundary.
8

## Slide 9
Uncertainty, Latency, and Terrain
Why attacks can hide
Q_k = g(r_k, sigma_IMU, sigma_v, Delta t_k)
Feature meanings
r_k: GPS vs dead-reckoning residual
sigma_IMU: vibration / yaw variability
sigma_v: velocity variance
Delta t_k: arrival timing stress + packet age
Latency behavior now implemented
Buffered latency changes packet timing stress.
Higher latency increases Q_k, S_k, and epsilon_min.
This supports preliminary synthetic rehearsal before hardware.
higher latency / rough terrain -> larger S_k -> larger epsilon_min -> harder detection
9

## Slide 10
Attack Models
Semantic GPS manipulation
Step bias
Add fixed displacement to GPS.
Cleanest validation for epsilon_min.
Sweep: 0.5, 1, 2, 3, 5, 7.5, 10 m.
Replay
Replay old valid GPS stream.
Tests temporal manipulation.
No packet-format anomaly required.
Freeze
Hold GPS at one coordinate.
Simulates stale or locked sensor.
Divergence grows as rover moves.
Random drift
Slow false movement over time.
Useful for gradual semantic manipulation.
Implemented for synthetic tests.
All attacks enter before GPS update -> innovation changes -> detector responds
10

## Slide 11
What Has Been Built Till Now
Phase 0 implementation
Core software
EKF, kinematics, detector, uncertainty estimator.
Telemetry parser, receiver, logger, plotter.
Synthetic rover and latency simulator.
Experiment tools
Full 2^3 matrix automation.
Step-bias sweeps.
Attack injector for step, replay, freeze, drift.
Analysis tools
Threshold locking from nominal CSVs.
Empirical P_D summaries.
ROC and detection-probability plots.
Random Forest uncertainty-training stub.
Docs and repo state
Math framework, telemetry protocol, running guide, GPS notes, roadmap.
Tests pass: 8 automated checks.
Committed cleanly: 61216fb.
11

## Slide 12
Current Status and Readiness
What is complete vs pending
Software / Phase 0 90-95% complete
Math implementation 80-85% aligned
Experimental validation awaiting hardware
The build phase is mostly complete; the remaining project value comes from real UGV01 data.
Core digital-twin code should not need a rewrite after hardware arrives.
Expected changes: real GPS parsing, calibrated rover constants, threshold from real nominal data, learned Q_k from real runs.
12

## Slide 13
What Remains After UGV01 Arrives
Integration and evidence
Hardware integration
Assemble rover.
Wire BN-220 GPS, encoders, IMU.
Verify packet CRC and sequence continuity.
Calibration
Wheel radius, wheel base, ticks/rev.
Straight-line and turn tests.
Stationary GPS noise and HDOP behavior.
Validation
40 benign baseline runs.
Threshold locking and learned uncertainty.
Attack campaign and detectability maps.
packets -> calibration -> benign baselines -> threshold locking -> learned uncertainty -> attacks -> results
13

## Slide 14
Future Work Roadmap
Last slide
1
Bring-up
UGV01 assembly, BN-220 GPS, encoder/IMU telemetry, CRC-valid packets
2
Calibrate
Wheel geometry, GPS noise, local-frame conversion, straight and turn tests
3
Baseline
Full 2^3 benign matrix: speed, terrain, latency, 5 trials each
4
Learn
Lock threshold, train Q_k estimator, compare adaptive vs fixed EKF
5
Attack
Step sweep, replay, freeze; compute P_D, ROC, detection delay
6
Publish
Detectability maps, confidence envelopes, results, limitations, manuscript
Final aim: quantify when GPS attacks are detectable, degraded, or effectively hidden by mobility-induced uncertainty.
14